## Slide 1
ROS 2 Nav2
Node Graph Analysis
Full navigation stack extracted from rqt_graph · rosgraph.dot
22
Active Nodes
30+
Topics
30+
Action Servers
8
Nav2 Servers
KEY NODES
/bt_navigator
/planner_server
/controller_server
/behavior_server
/slam_toolbox
/collision_monitor
/velocity_smoother
/docking_server
/route_server
/waypoint_follower
/smoother_server
/lifecycle_manager_navigation
Full Nav2 Jazzy stack · Gazebo simulation bridge · Custom nodes: /lidar_monitor /patrol

## Slide 2
System Architecture Overview
Five functional layers from sensor input to actuator output
01 SENSOR INPUT
/ros_gz_bridge
Gazebo simulation bridge — translates gz-transport to ROS 2 topics for the full navigation stack
Publishes: /scan /odom /imu /joint_states /tf
02 LOCALIZATION & MAPPING
/slam_toolbox · /robot_state_publisher
SLAM builds the occupancy grid and maintains coordinate frame transforms consumed by costmaps and planners
Publishes: /map /pose /tf (map→odom) /robot_description
03 COSTMAP LAYERS
/global_costmap/global_costmap · /local_costmap/local_costmap
Global costmap (static + obstacle layers) for path planning; Local costmap (voxel layer) for reactive control
Consumes: /map /scan /odom — Publishes: costmap costmap_raw published_footprint
04 PLANNING & CONTROL
/planner_server · /controller_server · /smoother_server · /route_server
Planner computes global paths; Controller executes them; Smoother refines; Route server provides graph-based routing
/plan /cmd_vel_nav /plan_smoothed /speed_limit /route_graph
05 SAFETY & ACTUATOR
/velocity_smoother · /collision_monitor · /ros_gz_bridge
Velocity smoother applies acceleration limits; Collision monitor enforces safety zones before final /cmd_vel output
/cmd_vel_nav → /cmd_vel_smoothed → /cmd_vel → robot

## Slide 3
Nav2 Core Servers
The eight primary Nav2 lifecycle nodes and their responsibilities
/bt_navigator
Mission Executive
Receives /goal_pose + /odom · Runs behavior trees via two rclcpp nodes (navigate_to_pose, navigate_through_poses) · Publishes navigate_to_pose and navigate_through_poses actions
/planner_server
Global Path Planner
Serves /compute_path_to_pose and /compute_path_through_poses actions · Publishes /plan (Path) · Consumes global costmap + map TF
/controller_server
Local Path Follower
Serves /follow_path action · Subscribes /odom + /speed_limit · Publishes /cmd_vel_nav /local_plan /transformed_global_plan /evaluation
/behavior_server
Recovery Behaviors
Serves spin / backup / wait / drive_on_heading / assisted_teleop · Subscribes /cmd_vel_teleop · Publishes /cmd_vel_nav for recovery motions
/smoother_server
Path Smoother
Serves /smooth_path action · Consumes /global_costmap/costmap_raw + footprint · Publishes /plan_smoothed
/waypoint_follower
Waypoint Sequencer
Serves /follow_waypoints and /follow_gps_waypoints actions · Orchestrates multi-goal missions via navigate_to_pose action
/route_server
Graph-Based Router
Serves /compute_route and /compute_and_track_route · Publishes /plan /route_graph /speed_limit · Consumes global costmap
/lifecycle_manager_navigation
Lifecycle Coordinator
Manages lifecycle transitions for all Nav2 servers · Publishes /bond (heartbeat) and /diagnostics · Orchestrates startup/shutdown order
All servers communicate lifecycle state via /bond topic and publish /transition_event on state changes

## Slide 4
Sensor Input & Hardware Bridge
ROS-Gazebo bridge publishes all sensor data — consumed across the navigation stack
/ros_gz_bridge
Gazebo ↔ ROS 2 Transport
CONSUMES: /cmd_vel (Twist)
/scan
LaserScan
Consumers: slam_toolbox · global_costmap · local_costmap · collision_monitor · lidar_monitor
/odom
Odometry
Consumers: bt_navigator · controller_server
/imu
Imu
Consumers: ros_gz_bridge only (published)
/joint_states
JointState
Consumers: robot_state_publisher
/tf
TFMessage
Consumers: smoother_server · bt_navigator · behavior_server · collision_monitor · docking_server · route_server
/robot_state_publisher
/scan is the most consumed topic in the system — feeds 5 subscribers simultaneously

## Slide 5
Velocity Command Pipeline
How navigation commands flow from planners to the robot drive
1
/controller_server
→ publishes /cmd_vel_nav
DWB/MPPI planner executes path following
Also: /behavior_server publishes /cmd_vel_nav for recovery behaviors
2
/velocity_smoother
→ publishes /cmd_vel_smoothed
Applies acceleration and deceleration limits
Subscribes /cmd_vel_nav · Publishes /cmd_vel_smoothed
3
/collision_monitor
→ publishes /cmd_vel
Final safety gate — checks /scan + /local_costmap/published_footprint
Subscribes /cmd_vel_smoothed · Publishes /cmd_vel (the actuator command)
4
/ros_gz_bridge
→ publishes → Robot
Receives /cmd_vel and forwards to Gazebo diff-drive plugin
In Phase 5: sends directly to TurtleBot3 hardware over WiFi DDS
BYPASS: /docking_server also publishes /cmd_vel directly (bypasses velocity smoother during dock/undock maneuvers)
Two sources of /cmd_vel_nav: controller_server (normal navigation) and behavior_server (recovery)

## Slide 6
Costmap Architecture
Global and local costmaps — both publish 15+ internal diagnostic topics
/global_costmap
Subscribes: /map (OccupancyGrid)
Subscribes: /scan (obstacle detection)
Subscribes: /global_costmap/footprint
Layers:
static_layer
obstacle_layer
Consumers:
/smoother_server (costmap_raw)
/route_server (costmap_raw)
Key outputs: costmap · costmap_raw · published_footprint · static_layer · obstacle_layer (+ raw/updates variants)
/local_costmap
Subscribes: /scan (LaserScan)
Subscribes: /local_costmap/footprint
Layers:
voxel_layer (3D obstacle)
Consumers:
/behavior_server (costmap_raw)
/docking_server (costmap_raw)
/collision_monitor (published_footprint)
Unique: voxel_grid + clearing_endpoints
Key outputs: costmap · costmap_raw · published_footprint · voxel_layer (+ raw/updates variants)
Local costmap uses voxel_layer (3D) vs global's obstacle_layer (2D) — local_costmap feeds behavior/docking/collision nodes

## Slide 7
Custom & Auxiliary Nodes
Project-specific nodes extending the standard Nav2 stack
/lidar_monitor
Custom LiDAR safety node
Subscribes: /scan (LaserScan, reliable QoS)
Publishes: /closest_obstacle (Float32, 5 Hz)
Function: Extracts minimum obstacle distance from LiDAR scan — provides lightweight safety metric without full costmap overhead
/patrol
Autonomous waypoint patrol agent
Subscribes: /navigate_to_pose/_action/status
Subscribes: /navigate_to_pose/_action/feedback
Subscribes: /estop (Bool, RELIABLE+TRANSIENT_LOCAL)
Function: Nav2 action client cycling hardcoded map-frame waypoints — cancels goal on e-stop signal
/docking_server — Full Nav2 Docking Stack
Subscribes
/detected_dock_pose
/navigate_to_pose/_action/status + feedback
/local_costmap/costmap_raw + footprint
Publishes
/cmd_vel (direct actuator bypass)
/dock_pose /filtered_dock_pose
/staging_pose /docking_trajectory
Action Servers
/dock_robot (_action/status + feedback)
/undock_robot (_action/status + feedback)
Also: /docking_server/transition_event
/docking_server publishes /cmd_vel directly — bypassing velocity_smoother for precise dock alignment

## Slide 8
Action Server Map
All ROS 2 actions active in this graph — organized by server
/bt_navigator
/navigate_to_pose
/navigate_through_poses
/planner_server
/compute_path_to_pose
/compute_path_through_poses
/controller_server
/follow_path
/behavior_server
/spin
/backup
/wait
/drive_on_heading
/assisted_teleop
/smoother_server
/smooth_path
/waypoint_follower
/follow_waypoints
/follow_gps_waypoints
/route_server
/compute_route
/compute_and_track_route
/docking_server
/dock_robot
/undock_robot

## Slide 9
Graph Analysis Summary
Key observations from the rqt_graph / rosgraph.dot analysis
01
Full Nav2 Jazzy Stack Active
All standard Nav2 servers are running: bt_navigator, planner_server, controller_server, behavior_server, smoother_server, route_server, waypoint_follower, docking_server — plus lifecycle_manager_navigation.
02
Layered Velocity Pipeline
cmd_vel_nav → velocity_smoother → cmd_vel_smoothed → collision_monitor → cmd_vel → ros_gz_bridge. Docking server bypasses smoother for precise dock alignment.
03
Route Server Present (Nav2 Extras)
The /route_server indicates a graph-based routing capability beyond basic A* planning — supports /compute_route and /compute_and_track_route for structured environments.
04
Custom Nodes Integrated
/lidar_monitor (closest_obstacle at 5 Hz) and /patrol (autonomous waypoint cycling with e-stop) are project-specific nodes woven into the Nav2 action framework.
05
BT Navigator Split
bt_navigator spawns two separate rclcpp nodes: bt_navigator_navigate_to_pose_rclcpp_node and bt_navigator_navigate_through_poses_rclcpp_node — each independently subscribing to all relevant action feedback topics.
06
/bond Heartbeat Pattern
All lifecycle nodes publish /bond (heartbeat) and subscribe to it — lifecycle_manager_navigation monitors all bonds to detect node failures and trigger managed recovery.
22 active nodes · 37+ topics · 14 action servers · Full Nav2 Jazzy + custom patrol/monitor nodes