## Slide 1
🤖
TurtleBot3 Burger
Phase 5: Hardware Deployment
TurtleBot3
System Architecture
ROS 2 Jazzy · Gazebo Harmonic · Docker · Nav2 · SLAM
2
Containers
6
Subsystems
9+
ROS Topics
7
Launch Files
Simulation-first · Docker-isolated · Hardware-ready

## Slide 2
System Overview
Two Docker containers — simulation on host, hardware on RPi 4
turtlebot3_simulator
osrf/ros:jazzy-desktop-full · network_mode: host · Fast-DDS
🌐 Gazebo Harmonic
Physics + sensors + GUI
🔗 ROS ↔ Gazebo Bridge
ros_gz_bridge + robot_state_publisher
🚀 tb3_bringup
7 launch file orchestrations
📡 tb3_monitor
lidar_monitor · health_monitor · mock_battery
🎮 tb3_controller
Gamepad · wanderer · patrol · keyboard
🗺️ Autonomous Stack
slam_toolbox + Nav2
turtlebot3_robot [Phase 5]
robotis/turtlebot3:jazzy-sbc-latest
RPi 4 (arm64) · WiFi DDS
🤖 TurtleBot3 Burger
Hardware + OpenCR
WiFi · Fast-DDS (Phase 5)
Host Machine
Ubuntu 24.04
F310 Gamepad @ /dev/input/js0
All simulation runs in Docker with network_mode: host for low-latency DDS communication

## Slide 3
Gazebo Harmonic + ROS Bridge
Physics simulation ↔ ROS 2 topic translation layer
🌐 Gazebo Harmonic
gz server
Physics engine + sensor simulation
Publishes: /scan /odom /imu /tf via gz-transport
gz GUI client
Graphical viewport renderer
Skipped when headless:=true
gz-transport
(loopback)
🔗 Bridge Layer
ros_gz_bridge
Bidirectional topic bridge (bridge_params.yaml)
7 topic mappings incl. /cmd_vel as Twist
robot_state_publisher
URDF → /tf_static
Publishes TurtleBot3 link tree static frames
Key ROS Topics Bridged
/scan
Gz→ROS · LaserScan
wanderer, lidar_monitor, SLAM, Nav2
/cmd_vel
ROS→Gz · Twist
gamepad_manager, wanderer, Nav2, keyboard
/odom
Gz→ROS · Odometry
scan_action_server, Nav2
/imu
Gz→ROS · Imu
health_monitor
bridge_params.yaml defines all topic mappings — /cmd_vel uses geometry_msgs/Twist (not TwistStamped)

## Slide 4
tb3_controller
Input handling, e-stop gating, and autonomous motion commands
🎮 Gamepad Chain (F310)
joy_node
/dev/input → /joy
@ 20 Hz
teleop_twist_joy
/joy → /cmd_vel_raw
RB=deadman, LB=turbo
gamepad_manager
/cmd_vel_raw → /cmd_vel
B=stop A=clear Y=shutdown
/estop RELIABLE+TRANSIENT_LOCAL → wanderer, patrol
🔄 wanderer
Reactive obstacle avoidance
/scan + /estop → /cmd_vel
forward / turn / stop state machine
📍 patrol
Nav2 waypoint client
Cycles hardcoded map-frame waypoints
Cancels on /estop
🔭 scan_action_server
360° rotation action server
/tb3_scan_360 using odom feedback
Available for future use
⌨️ teleop_twist_keyboard
Keyboard teleoperation
→ /cmd_vel (requires TTY)
Direct bypass of e-stop
E-stop uses RELIABLE + TRANSIENT_LOCAL QoS — new subscribers receive the last latched value on connect

## Slide 5
tb3_monitor
Telemetry, health reporting, and safety sensing
📡 lidar_monitor
Input: /scan (LaserScan)
Output: /closest_obstacle (Float32)
Rate: 5 Hz — minimum distance extraction
❤️ health_monitor
Input: /battery_state + /imu
Logs: voltage, charge %, IMU orientation
Passive observer — no output topics
🔋 mock_battery
Output: /battery_state @ 1 Hz
Simulates BatteryState message
For testing without real hardware
🔍 tf2_verifier
Debug utility only — not production
Verifies map→base_link TF chain
Checks freshness + completeness
/scan → lidar_monitor → /closest_obstacle → health_monitor | mock_battery → /battery_state → health_monitor
lidar_monitor runs at 5 Hz to reduce CPU load while still detecting obstacles in real-time

## Slide 6
Autonomous Stack
SLAM mapping + Nav2 navigation — work together to enable full autonomous operation
🗺️ slam_toolbox
Mode: online_async
Input:
/scan (LaserScan)
Output:
/map (OccupancyGrid)
TF:
map → odom transform
Resolution:
0.05 m/cell
Max Range:
3.5 m
Solver:
Ceres (loop closure on)
🧭 Nav2 Stack
bt_navigator + DWB local planner
Input:
/map + map→odom TF from SLAM
Action:
/navigate_to_pose
Output:
/cmd_vel (Twist)
Robot radius:
0.105 m (TB3 Burger)
Max vel:
0.22 m/s
Planner:
DWB local planner
/map
+TF
Configuration Files
slam_params.yaml — 0.05m resolution · 3.5m max range · Ceres solver · loop closure enabled
nav2_params.yaml — robot_radius=0.105m · max_vel_x=0.22m/s · DWB local planner
Nav2 requires SLAM to be running first — map→odom TF must be publishing before bt_navigator starts

## Slide 7
Launch File Orchestration
tb3_bringup — 7 composable launch files for different operating modes
sim_bringup.launch.py
Foundation: Gazebo world + bridge + RSP
Starts: gz server, ros_gz_bridge, robot_state_publisher
sim_house.launch.py
Same as sim_bringup, indoor world
Starts: gz server, ros_gz_bridge, robot_state_publisher
gamepad.launch.py
F310 gamepad teleoperation
Starts: joy_node, teleop_twist_joy, gamepad_manager
teleop.launch.py
Keyboard driving (requires TTY)
Starts: teleop_twist_keyboard
wanderer.launch.py
Reactive obstacle avoidance
Starts: lidar_monitor, wanderer
slam.launch.py
Mapping only, no Nav2
Starts: slam_toolbox (online_async)
nav2.launch.py
Full navigation (needs SLAM running)
Starts: Nav2 stack (bt_navigator + DWB)
capability_demo.launch.py
Full M3 demo stack, mode selectable
Starts: SLAM + Nav2 + lidar_monitor + patrol|wanderer
capability_demo.launch.py is the one-shot command for full autonomous demos — use mode:=patrol or mode:=wanderer

## Slide 8
Key ROS Topics
The communication backbone connecting all subsystems
/scan
Gz→ROS
LaserScan
LiDAR point cloud — consumed by wanderer, lidar_monitor, slam_toolbox, Nav2 costmap
/cmd_vel
ROS→Gz
Twist
Drive commands — produced by gamepad_manager, wanderer, Nav2, or keyboard teleoperation
/cmd_vel_raw
internal
Twist
Pre-e-stop gamepad velocity from teleop_twist_joy, gated by gamepad_manager
/joy
HW→ROS
Joy
Raw F310 gamepad state from joy_node — consumed by teleop_twist_joy and gamepad_manager
/estop
internal
Bool
E-stop signal with RELIABLE+TRANSIENT_LOCAL QoS — latched, consumed by wanderer and patrol
/map
internal
OccupancyGrid
SLAM-generated occupancy map — published by slam_toolbox, consumed by Nav2 global costmap
/odom
Gz→ROS
Odometry
Gazebo DiffDrive odometry — consumed by scan_action_server and Nav2
/battery_state
sim
BatteryState
Mock battery telemetry — published by mock_battery at 1 Hz, consumed by health_monitor
/closest_obstacle
internal
Float32
Minimum LiDAR distance at 5 Hz from lidar_monitor — consumed by health_monitor
All topics flow through the ros_gz_bridge — /cmd_vel is the single actuator command topic bridged to Gazebo

## Slide 9
Architecture Summary
Simulation-first, hardware-ready, modular by design
01
Docker Isolated
Two containers cleanly separate simulation from hardware. The same ROS 2 nodes run on RPi 4 in Phase 5 with no code changes.
02
Bridge Pattern
ros_gz_bridge decouples ROS from Gazebo internals. Topic mappings in bridge_params.yaml are the single source of truth.
03
E-Stop Safety
RELIABLE + TRANSIENT_LOCAL QoS means every node joining late still receives the last e-stop state — no race conditions.
04
SLAM + Nav2 Pipeline
slam_toolbox publishes the map and map->odom TF that Nav2 depends on. Launch order is enforced via launch file dependencies.
05
Composable Launches
7 independent launch files can be combined or run standalone. capability_demo.launch.py is the single full-stack entry point.
06
Simulation Fidelity
Gazebo Harmonic provides physics-accurate LiDAR, odometry, and IMU — making sim-to-real transfer straightforward.
Phase 5: Connect turtlebot3_robot container via WiFi DDS — all ROS nodes remain unchanged